## Slide 1
ARDUINO-BASED OVERLOAD PROTECTION SYSTEM FOR TRANSFORMERS
GUIDED BY:
Mr. N Selvam M.E
Assistant Professor /EEE
PRESENTED BY:
  NALIN KUMAR S P (927622BEE073)
  SANJAAI U N (927622BEE094)
  SHARMITHA S P (927622BEE106)
DEPARTMENT OF ELECTRICAL AND ELECTRONICS ENGINEERING
18EEP301L-MINOR PROJECT III
FIRST REVIEW
YEAR/ SEMESTER – III/V
BATHCH NO :12
DATE:24/09/2024

## Slide 2: Abstract:
This project presents an Arduino-based overload and temperature protection system designed to prevent transformers from damage due to excessive load and overheating. The system continuously monitors the current and temperature of the transformer using a current sensor and a temperature sensor, respectively. If the load exceeds a predefined threshold or if the temperature rises beyond a safe limit, the Arduino triggers a relay to disconnect the transformer from the load. This dual protection mechanism enhances the reliability and longevity of transformers in power distribution networks, offering a cost-effective and efficient solution for transformer protection.

## Slide 3: Introduction
Transformers are essential for voltage regulation in power distribution networks.
They are susceptible to overload and overheating, which can cause significant damage and reduce their lifespan.
Objective: Develop an Arduino-based protection system that monitors load and temperature, ensuring the safety and longevity of transformers by disconnecting them under critical conditions.

## Slide 4: Problem Statement
Transformers are important for power distribution but can be easily damaged by overload and overheating. Can cause excessive heating, leading to insulation failure and transformer burnout.
Overload: Can cause excessive heating, leading to insulation failure and transformer burnout.
Overheating: Long exposure to high temperatures can damage materials, lower efficiency, and shorten lifespan.
Current Systems: Traditional protection methods may not always provide real-time monitoring or rapid response.
Need: A cost-effective, real-time monitoring system that can automatically protect transformers from these issues.

## Slide 5: Project Objective
Primary Goal: To design and implement an Arduino-based system that provides real-time protection for transformers against overload and overheating.
Specific Objectives:
  Monitor Load: Continuously track the current passing through the transformer using a current sensor.
  Monitor Temperature: Measure the transformer's temperature using a temperature sensor.
  Automatic Protection: Disconnect the transformer from the load using a relay when critical thresholds are exceeded.
  Cost-Effectiveness: Develop a solution that is affordable and easy to implement for widespread use in power distribution networks.

## Slide 6: Block diagram

## Slide 7: Working Principle
Monitoring:
  The current sensor (ACS712) continuously measures the current flowing through the transformer.
  The temperature sensor (LM35) monitors the transformer’s temperature.
Data Processing:
  The Arduino receives data from the sensors.
  It compares the readings with predefined safety thresholds.

## Slide 8
Protection:
  If the current or temperature exceeds safe levels, the Arduino triggers the relay module.
  The relay disconnects the transformer from the load to prevent damage.
Reset:
  The system remains disconnected until the issue is resolved, and the system is reset.

## Slide 9: System Overview
Components:
  Arduino: Controls the system.
  Current Sensor: Measures load current.
  Temperature Sensor: Measures transformer temperature.
  Relay: Disconnects the transformer if needed.
Function:
  Monitor: Continuously checks current and temperature.
  Protect: Automatically disconnects transformer if thresholds are exceeded.

## Slide 10: transformer
Definition:
A transformer is an electrical device that transfers electrical energy between two or more circuits using electromagnetic induction.
Basic Principle:
Operates on the principle of electromagnetic induction, where a varying current in the primary coil generates a varying magnetic flux, which induces a voltage in the secondary coil.
Purpose: Used to increase (step-up) or decrease (step-down) AC voltages in power transmission and distribution.
Applications: Power distribution, electrical isolation, impedance matching, voltage regulation in various electrical systems.

## Slide 11: Arduino Microcontroller
Definition:
Arduino Microcontroller is a programmable device that acts as the brain of an electronic system. It processes inputs from sensors and controls outputs like motors, lights, or relays based on the programmed instructions.
Role: Central controller for the protection system.
Key Features:
  Analog Inputs: Reads data from current and temperature sensors.
  Digital Outputs: Controls the relay based on sensor readings.
  Custom Code: Manages sensor data and decision-making logic.
  Communication: Potential for data logging or remote monitoring.

## Slide 12: Current Sensor
Function: Measures the electrical current flowing through the transformer.
Sensor Name: ACS712 Hall Effect Sensor
IC: ACS712
Connection: Outputs an analog voltage proportional to the current, which is read by the Arduino.
Purpose: Detects overload conditions by monitoring current levels and triggering protective actions if thresholds are exceeded.

## Slide 13: Temperature Sensor
Function: Monitors the temperature of the transformer.
Sensor Name: LM35 Temperature Sensor
IC: LM35
Connection: Provides an analog output voltage proportional to the temperature, which is read by the Arduino.
Purpose: Detects overheating by continuously measuring the transformer’s temperature, ensuring it remains within safe operating limits.
Note: The LM35 is known for its accuracy and simplicity in temperature measurement.

## Slide 14: Relay Module
Definition:
A relay is an electrically operated switch that uses an electromagnet to mechanically operate a switch, enabling the control of a high-power circuit with a low-power signal.
Function: Controls the connection and disconnection of the transformer from the load.
Relay Type: 5V Single-Channel Relay Module
Connection: Connected to the Arduino, which sends a signal to trigger the relay based on sensor data.
Purpose: Automatically disconnects the transformer to prevent damage when overload or overheating is detected.

## Slide 15: Circuit Diagram

## Slide 16: at normal loaded condition

## Slide 17: at overloaded condition

## Slide 18: Cost estimation
s.no | Name of the components | quantity | cost
01 | Arduino UNO | 1 | 650
02 | Current sensor | 1 | 250
03 | Temperature sensor | 1 | 150
04 | Relay module | 1 | 100
05 | Bulb and Holder | Each 1 | 100
06 | LCD display | 1 | 650
07 | other |  | 700
 |  | Total | 2600

## Slide 19: reference
Allegro Microsystems. ACS712 Current Sensor Datasheet. Retrieved from:
https://www.allegromicro.com
Texas Instruments. LM35 Temperature Sensor Datasheet. Retrieved from:
https://www.ti.com/lit/ds/symlink/lm35.pdf
Arduino. Arduino Programming Language Reference. Retrieved from:
https://www.arduino.cc/reference/en/
Spark Fun. Relay Module Guide. Retrieved from:
https://www.sparkfun.com
S. Rao, Power Transformer Maintenance.
Khanna Publishers, 2019.

## Slide 20: Conclusion
This Arduino-based system successfully protects transformers from overload and overheating in a simple and cost-effective way.
It monitors the current and temperature in real-time to prevent damage to the transformer.
The system uses ACS712 (current sensor), LM35 (temperature sensor), and a relay to automatically disconnect the transformer if the current or temperature is too high.
This project shows that using Arduino can improve transformer safety and reliability in power systems.

## Slide 21
THANK YOU
THANK YOU